## Slide 1: Scenarios and Deployment Considerations for High Performance Wide Area Network
Junfeng Zhao - CAICT(zhaojunfeng@caict.ac.cn)
IETF 122 HPWAN sidemeeting, March 2025

## Slide 2: Agenda
Introduction
Typical Scenarios for HP-WANs
Deployment Considerations for HP-WANs
Comments and questions

## Slide 3: Introduction
HP-WAN performance requirements for WANs:
low or zero packet loss rate
low latency,
high throughput
low CPU utilization,
Challenges for the high performance in long-distance and wide area networks deployment
  the high utilization and high throughput capabilities for long distance links;
  the efficient congestion control mechanisms to avoid packet loss;
  fair sharing of link bandwidth resources among multiple concurrent applications;
  the packet ACK delay increases with distance, which will be challenging for high-performance applications, especially distributed processing models.

## Slide 4: Typical Scenarios for HP-WANs
  Collaborative and Interactive Data Transmission
  Long-distance Data Transmission
massive research data transmission between HPCs
distance range from 100km to 1000km;
regularly or in demand, data volume from a few terabytes to several hundred terabytes;
Balance on Data transmission costs and security
The US ESnet6 and the EU EuroHPC …...
data transmission of training samples between the DCs for AI
distance range from n*100km to 1000skm;
in demand
training large models in the billions or trillions tokens for N*100 terabytes to P of corpus data.
WAN
Site A
Site B
>1000KM
MAN
Core DC
Core DC
Edge DC or host
Edge DC
or host
Edge DC or host
80KM~100KM
data transmission between storage and computing separation data centers
For energy limitation, deploy multiple DC with storage and computing separated in MAN ,e.g. In 2023, Amazon@100Gbps&100 kilometers;
To avoid data leakage , storage in the customer's private DC and connected to the provider's DC for AI training through a wan.
high-throughput data transmission between DCs under distributed intelligent computing
Distributed Ai inference: AI inference at edge DCs with high user Experience;
Distributed Ai training: Distributed Compute Aggregation.

## Slide 5: Deployment Considerations for HP-WANs(1)
  1. Host Optimization Deployment
DCN or  dedicated-line
WAN（LOSSSY）
DCN or dedicated-line
The NIC with HP-WAN protocol optimization
The NIC with HP-WAN protocol optimization
Host A
Host B
improved transport layer protocol on the NIC of host server to achieve long-distance and efficient transmission based on lossy networks.
optimize the transport layer protocol may involve caching and resembling for out of order packages, packet loss tolerant and error correction mechanism based on lossy network, etc.

## Slide 6: Deployment Considerations for HP-WANs(2)
  2. WAN optimization Deployment
optimize the performance of packet loss, bandwidth utilization and latency to provide high-throughput data transmission between DCs .
The optimization of wide area networks may involve path selection, congestion control and flow control etc.
DCN or dedicated-line
WAN（LOSSSY）
DCN or dedicated-line
The optimization of packet loss, out of order, delay and jitter in HPWAN
Host A
Host B

## Slide 7: Deployment Considerations for HP-WANs(2)
  3. Gateway Deployment
deploy gateway devices at the DC edge to isolate or relay traffic within the data center and wide area network.
The gateway devices should support high-performance services packet caching, buffering, and retransmission, and
Implement the collaboration and Interaction between gateway and WAN through running optimized high-performance transport layer protocols optimize the performance of packet loss, bandwidth utilization and latency to provide high-throughput data transmission between DCs .
The optimization of wide area networks may involve path selection, congestion control and flow control etc.
Gateway
WAN（LOSSSY）
Host A
Host B
Gateway
DCN
DCN

## Slide 8: Comparison and Analysis for HPWAN Deployment
Potential deployment solutions | Challenges | Scenario | Distance | Bandwidth | Timeliness
Host Optimization Deployment | Interoperability challenges with multi-vendor network NICs and switches | On -demand , decentralized ,medium and low-speed ， cost-effectiveness | 80~ 100KM | N*10G~ | medium/low
WAN optimization Deployment | Need to network transformation and update | Ultra-long-distance interconnection + large-scale interconnection | Over 1000KM~ | Over 100G | medium/high
Gateway Deployment | scalability limitation, increase investment and potential failure points. | Long-distance interconnection + medium-scale interconnection | Over 1000KM~ | Over N*10~N*100G | medium/high
The “network” and “ Host ” alone encounter Challenges, “network” and “ Host ” collaboration may be good choices!

## Slide 9
Comments and questions
Comments and questions are very welcome!

## Slide 10
Thank You